MASTERSPEC - SECTION 31 32 39

SOIL NAILING ACCESSORIES

GENERAL

SUMMARY

Section Includes:  Soil nailing tendon accessories indicated, specified, or required to complete installation.

SUBMITTALS

Product Data:  Manufacturers technical literature for each type of manufactured material and product specified.

Certification:  Manufacturer’s written certification that products furnished comply with or exceed specified requirements.

QUALITY ASSURANCE

Manufacturer Qualifications:  Company specializing in manufacturing products specified with minimum of three years documented experience.

DELIVERY, STORAGE, AND HANDLING

Store and handle materials to prevent damage.

PRODUCTS

MANUFACTURER

PIERESEARCH®, 501 East Main Street, Arlington TX, 76010; phone (800) 342-2409; (817) 277-3738; Fax (817) 275.2335; www.pieresearch.com.

For manufacturers not listed, submit as substitution according to the Conditions of the Contract and Division 01 Specification Sections.

TENDON CENTRALIZERS (QUICK-LOCK® UNIBAR® CENTRALIZERS)

Description:

Centralizer is made of plastic and are two identical halves that can be easily snapped together around soil nail tendon.

Centralizer keeps soil nail tendon centered in drilled shaft and does not impede flow of grout/concrete.

Centralizer Part Numbers:

NOTE TO SPECIFIER:  SELECT ONE OF THE FOLLOWING OPTIONS:

4-6UBC:	4" O.D. Quick-Lock® Unibar® Centralizer #5 - #6

4-8UBC:	4" O.D. Quick-Lock® Unibar® Centralizer #7 - #8

4-1.5IN-UBC:	4" O.D. Quick-Lock® Unibar® Centralizer with 1.5" I.D. Hub

4-2IN-UBC:	4" O.D. Quick-Lock® Unibar® Centralizer with 2" I.D. Hub

4-2.5IN-UBC:	4" O.D. Quick-Lock® Unibar® Centralizer with 2.5" I.D. Hub

6-6UBC:  	6" O.D. Quick-Lock® Unibar® Centralizer #5 - #6

6-8UBC:  	6" O.D. Quick-Lock® Unibar® Centralizer #7 - #8

6-1.5IN-UBC:	6" O.D. Quick-Lock® Unibar® Centralizer with 1.5" I.D. Hub

6-2IN-UBC:	6" O.D. Quick-Lock® Unibar® Centralizer 2" I.D. Hub

6-2.5IN-UBC:	6" O.D. Quick-Lock® Unibar® Centralizer 2.5" I.D. Hub

8-6/11UBC		8” O.D. Quick-Lock® Unibar® Centralizer Adjustable I.D. Hub

fits rebar sizes #6 thru #11

EXECUTION

INSTALLATION

Attach centralizers to soil nail tendon according to manufacturer’s instructions.

Snap two pieces together around soil nail tendon with one piece being inverted to the other piece.

Attachment Locations:

At deep end of drilled shaft, attach centralizer at approximately 1 foot from end of the soil nail tendon.

Attach centralizer at maximum 10 foot intervals along total length of soil nail tendon.

At access end of drilled shaft, attach centralizer so that it will be approximately 1 foot below grout/concrete surface.

To prevent sliding, secure centralizer to soil nail tendon with tie wire or zip tie threaded through end tab slots.

END OF SECTION